## Slide 1
MATLAB Tutorial for Reduced Order Representation of Microstructure
Yuksel C. Yabansu, PhD
September 25, 2017

## Slide 2: Local Microstructure Descriptor for Composites
: spatial bin
: local state
: volume fraction
: volume fraction of phase h in spatial cell s
Phases:
(1  white phase)
(2  gray phase)
1
2
3
5
4
6
7
8
9
10
11
15
14
13
16
12

## Slide 3: 2 Point Statistics
Spatial correlations capture all of the salient measures of the microstructure
Complete Set of for all possible

## Slide 4: Statistical Description of microstructure
Micrograph
2-point auto correlation
2-point correlation is the joint density of occurrence of local state and at material points separated by vector .
Can be computed conveniently using FFT algorithms.
More complex local states (crystal lattice orientation, tensorial variables, etc.) can be included in the definition.
Applicable to partial/incomplete datasets
Extensible for datasets with non-periodic/partially periodic datasets.

## Slide 5: Calculation of 2 point statistics
Two-point statistics expression is a convolution.
We take the FFT of both sides to take care of the summation faster than convolution in real space
The expression in top equation is nothing but a entry wise product in frequency space
After the product, we take inverse FFT to go back to real space to obtain 2-point statistics.

## Slide 6: Principal Component Analysis (PCA)
x
y
p1
p2
Original Axes
p1
p2
Principal Axes
p1
Reduced Axis
Obtain the first handful dimensions (out of possibly thousands or millions) that show the highest variation within the dataset.
Objective and hierarchical identification of most characteristic features.
Features are independent and uninformed of process and property.

## Slide 7: Principal Component Analysis (PCA)
where
are orthonormal basis vectors which count as unweighted microstructure features.
are PC weights and explicitly represents the microstructure.

## Slide 8: Install PyMKS
$ conda install -c conda-forge pymks scikit-learn=0.19 sfepy=2017.2 toolz scipy=0.19.1 matplotlib=2.0.2
$ conda install jupyter
$ conda install dask
$ conda install -c conda-forge bqplot
Link to tutorial:

## Slide 9: Documentation
Delineation of the space of 2-point correlations in a composite material system
http://www.sciencedirect.com/science/article/pii/S1359645408004886
Understanding and visualizing microstructure and microstructure variance as a stochastic process
http://www.sciencedirect.com/science/article/pii/S1359645411004654
Structure–property linkages using a data science approach: Application to a non-metallic inclusion/steel composite system
http://www.sciencedirect.com/science/article/pii/S1359645415001603
Versatile algorithms for the computation of 2-point spatial correlations in quantifying material structure
https://link.springer.com/article/10.1186/s40192-015-0044-x